## Slide 1: Intro to Satellite Imagery
Credit for Content belongs to:
Marcos de Jesus & Mo Fotouhi

## Slide 2: Satellite Imagery Overview
Remote Sensing
Acquiring information from a distance.
Earth and other planets are observed via remote sensors on satellites.
Sensors detect and record reflected or emitted electromagnetic energy.
Remote sensors provide:
  Global perspective
  Wealth of data
  Enable data-informed decision making based on the current and future state of our planet.
Credit: Nasa Earth Data

## Slide 3: Satellite Imagery Overview
Orbits
By cmglee - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=16891766
Different orbit altitudes have different applications
Low orbit
  180 km – 2,000 km
  Orbit time of 128 minute or less
  Remote Sensing(Planet and Sentinel)
Medium orbit
  2,000 km – 35,786 km(Geostationary orbit)
  Orbit time of 24 hours or less
  GPS and communication
High orbit
  > 35,786 km
  Orbit time of more than 24 hours
  Space exploration

## Slide 4: Satellite Imagery Overview
Sensors
Sun as source of illumination
Visible, infrared, thermal infrared, and microwave spectrum
Measure
  Land and sea surface temperature
  Vegetation Properties
  Imagery
Own source of illumination
Microwave spectrum
Measure:
  Vegetation structure
  Topography
  Sea-ice mapping

## Slide 5: Satellite Imagery Overview
Observing with the electromagnetic spectrum

## Slide 6: Satellite Imagery Overview
Multiple observed characteristics

## Slide 7: Satellite Imagery Overview
Red Edge Band

## Slide 8: Satellite Imagery Overview
Resolution
Spatial Resolution
Size of each pixel within the image and the area on Earth’s surface represented by it
Lower number = More detail
Temporal Resolution
The time it takes for a satellite to revisit the the same observation area
Metop Orbit. Credit: EUMETSAT

## Slide 9: Satellite Imagery Overview
Agricultural Use Case

## Slide 10: Satellite Imagery Overview
Challenges – Cloud Cover
cloud
cloud
Clouds block light – wrong values
Disrupts usual imagery schedule creating non-uniform data length and spacing

## Slide 11: Satellite Imagery Overview
Challenges – Varying Temporal Resolution
Days from Seeding
NDVI
Satellite Orbits and schedules
Cloud Coverage
Data cleaning and processing

## Slide 12: Available Free Satellite Imagery
Sentinel-1
Synthetic Aperture Radar
5 days temporal resolution
4 bands
5 meters resolution
Free
Sentinel-2
Optical
5 days temporal resolution
12 bands
20, 40 and 60 meters
Free

## Slide 13: Ordering & Working with Satellite Imagery
Satellite Imagery Service that provides a cloud data driver
Provides an API to order Satellite Imagery
Provides a GUI for browsing Satellite Imagery called EO Browser
https://www.sentinel-hub.com/
Sentinel Hub

## Slide 14: Ordering & Working with Satellite Imagery
Access to Sentinel-2 data is free
Stored in AWS S3 bucket
Searchable geospatially and temporally with Earth Search
Stored by individual bands in TIFF format
Can be downloaded locally
Acquiring Satellite Imagery

## Slide 15: Ordering & Working with Satellite Imagery
Working with Raster Data
Satellite bands are formatted as Raster data
Raster data is a matrix of cells organized in a grid where each cell contains a value
In Satellite Imagery the value contained is the bands value inside that cell for the image
The cells or pixels are geospatially referenced
Images Credit: https://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/what-is-raster-data.htm

## Slide 16: Ordering & Working with Satellite Imagery
Working with Raster Data – Band Arithmetic
The Raster format allows values across bands to be compared
Comparing values from different bands can make phenomena more apparent in imagery
NDVI is an example that makes vegetation stand out more in imagery
Image Credit: https://www.researchgate.net/figure/NDVI-data-in-Raster-form_fig5_332735913

## Slide 17: DEMO
https://github.com/thompsonalexdeere/purdue-satellite-imagery-demo

## Slide 18: Questions